## Slide 1
CG-MB
W221
Empty key Spaces
&
match new keys

## Slide 2
When we want to match a new key for the vehicle, find that the positions for key are full. At this time, we need to clear the positions，then match the new key.

## Slide 3
The first step
Calculate the password and erase the key位

## Slide 4
OBD connects the vehicle，choose“（EIS）”interface，click to read EIS data

## Slide 5
Read successfully，show that the positions for key are full

## Slide 6
Collect data first，compute password

## Slide 7
Default“Other key”，click ok

## Slide 8
please insert the key into EIS and click OK

## Slide 9
Please insert the key into the CG-MB device and click ok

## Slide 10
It is collecting with key，please wait ...

## Slide 11
Please insert the key into EIS and click ok

## Slide 12
please wait patiently for 10 seconds

## Slide 13
please pull out the key from the EIS, and then click ok

## Slide 14
please insert the key into the EIS again and click ok

## Slide 15
Pull out the key for 5 seconds, then insert into EIS, then click ok

## Slide 16
please insert the key into the CGMB device again and click ok

## Slide 17
Collection end，save data，default file name

## Slide 18
Save the file successfully

## Slide 19
Click“Upload data”

## Slide 20
Open the data just saved

## Slide 21
Upload data successfully

## Slide 22
Querying，please wait...

## Slide 23
Computing success，click ok

## Slide 24
Click 'Copy'

## Slide 25
Go to “（EIS）”，and copy the password

## Slide 26
Save the EIS data with password successfully

## Slide 27
Get erase password，wait a few seconds，show that calculated successfully

## Slide 28
Click“Wipe the EIS”

## Slide 29
please insert the simulation key into the EIS in 30 seconds......

## Slide 30
simulation key physical operation diagram

## Slide 31
Erase the EIS success，click ok

## Slide 32
Read EIS data again，show the related information after erasing

## Slide 33
Click ''Load EIS Data''

## Slide 34
Open the EIS data just saved

## Slide 35
Click“ Write EIS Data”

## Slide 36
Click ok

## Slide 37
please insert the simulation key into the EIS in 30 seconds

## Slide 38
simulation key physical operation diagram

## Slide 39
Write EIS data success

## Slide 40
Read EIS data again，showed as above picture

## Slide 41
Insert the original car key into the lock to learn and start

## Slide 42
Read EIS data again，left origin key position data only，erase key position data successfully

## Slide 43
The second step
Match new key

## Slide 44
Go to “Generate EE”，load EIS file just saved

## Slide 45
Load successfully，please check the information to see whether it is correct

## Slide 46
Click“Generate key file”，please wait......

## Slide 47
The key file was generated successfully，please save data file

## Slide 48
Go to “Read/write key”

## Slide 49
please insert the new key into CG-MB device

## Slide 50
Click ''read key''，show key information

## Slide 51
Click ''write''，please read the prompt carefully，click ok

## Slide 52
Choose一unused key position data，click and open it

## Slide 53
Write success

## Slide 54
please insert the new key into EIS to learn，start the car after learning

## Slide 55
Read EIS data again，show√，combine the car to start，match new key successfully！